## Slide 1
GESTURE BOT
Group 3:
Bjørn Sødal · Cornelius Brandt · Fynn Schilke ·
Maximilian Eckstein · Harshal Ghadge
Practical utilization of gesture recognition in motion-controlled robotics

## Slide 2
PROJECT IDEA
  Gesture-controlled mobile robot
  Enables more intuitive human–robot interaction
  Uses two-hand control: one for navigation, one for arm movement
  Provides live camera feedback for the operator

## Slide 3
CHALLENGES
Gesture recognition accuracy
Complicated Setup
3D positions
System Integration
02
Reliable gesture recognition under varying lighting conditions and hand orientations
Seamless communication between PC and robot (e.g. signal transmission problems)
3D hand tracking without depth sensors
Complex setup and compatibility issues across multiple PCs

## Slide 4
SOLUTIONS
  21 hand landmarks detected via MediaPipe
  Fast and accurate real-time recognition pipeline
  Hand-Landmark-Pipeline with pretrained model
  controlling robot velocities
  manages communication between RaspberryPi and PC
  Docker container for consistent, plug-and-play system setup
MediaPipe
ROS 2 Humble
MediaPipe 3D mapping
Docker
03
  MediaPipe provides simple 3D detection
  Estimating missing position data using 3D landmark projection (approximation, not full depth)
  Different approaches for arm movement (e.g. LiDAR-based or visual estimation) are currently being evaluated

## Slide 5
04
FUNCTIONAL REQUIREMENTS
USE-CASE SECNARIO
  Gesture-based movement control
  Gesture-based arm activation and positioning
  Real-time video feedback
“Trash Pickup” – robot identifies and picks up a nearby object

## Slide 6
DATASET & SYSTEM HARDWARE SETUP
DATASET
SYSTEM
  Based on a non-public MediaPipe dataset (Google)
  Pretrained neural network model for hand landmark detection
05
  TurtleBot3 Waffle Pi with Raspberry Pi 4
  ROS 2 Humble running on both PC and Pi (via Docker)
  Wi-Fi connection between PC and robot
  All computation handled on PC; Pi receives movement commands
  ROS Publisher–Subscriber architecture for modular design

## Slide 7
NEXT STEPS
PLANNING
OBSTACLES
  Integrate and test robotic arm control functionality
  Continue testing and troubleshooting of the ROS setup
  Finalize Docker container for easy deployment
  project report and preparing demonstration
No major changes in project timeline
06
  Occasional communication issues in university network
  Video output stability issues
  Outdated camera package dependencies

## Slide 9
THANK YOU
Questions & feedback are welcome!